Sample Basic Design Assumptions

Project: -----------------------

Task: Basic Assumptions for Structural Design

Basic Assumptions

- Building Structure Type	 		Class: 	I

- Design Codes				EBCS: 	1, 2, 3 and 8

Others: 	Euro Codes 2 & 3

- Design Method					Limit State Design Method

- Material Properties

Concrete					C – 25

Reinforcement Bars				S – 300

Earth Quake Zone				2

- Ground Properties

Soil Type					Black Cotton Soil

Bearing Capacity				150 Mpa

- Loads Considered

Roof Structures					Permanent, Imposed & Wind Loads

Plane Structures (Slabs and Stairs)		Permanent & Imposed Loads

Frame Structures				Permanent, Imposed & Earthquake

Loads

- Frame Structure Types				Unbraced Sway Frame

- Foundation Types					Isolated and Combined Footings

- Concrete Cover

Slab						15.0 cm

Beams and Columns				25, 40 cm

Footings					50 cm

- Factors Used

Materials					γc = 1.5; γs = 1.15

Loads						γG = 1.3; γQ = 1.6; γA = 1.0